## Slide 1: EVO192 High Security and Access Control Systems
www.paradox.com
Product Information

## Slide 2: EVO192 Overview
8 to 192-zone expandable security system
Built-in access control features (32 doors)
Supports PCS Series (PCS260/265) for GSM / GPRS communication
Multibus
Bus modules can be configured from the Panel
Allows to upgrade the firmware of multiple identical modules simultaneously through the combus
In-field upgrade caability for simple on-site updates
Supports Plug-In Voice Dialer (VDMP3)
Supports Internet Communication Module (IP150)
999 remotes with only one Transceiver [RTX3], programmable by the installer / Master user
New menu-driven zone programming method

## Slide 3: Overview
Digiplex EVO systems provide the highest level of protection
Designed to be easy to use
Modular concept
Provides installers with labour saving features
Makes expanding, installing, and servicing quick and convenient
Expand the system by adding plug-and-play expansion modules
Modules are connected to the combus
Modules can be configuered remotely
More processing power to offer more Users, zones, features, and flexibility

## Slide 4: EVO Features
Features | EVO192 / EVOHD
Maximum zones | 192
On-board zones | 8 (16 with ATZ)
Partitions | 8
User codes | 999
Panel In-Field firmware upgradeable | 
Access control (doors) | 32
Access levels / schedules | 16/32
Events buffered | 2048
PGMs | 250 (5 on board)
BUS modules | 254
Software | BabyWare / Neware / INSITE GOLD

## Slide 5: ComBus Architecture

## Slide 6: Keypad Modules
TM50 Touch Interactive Touchscreen
K656
Touch Sense Keypad
K641
32-Character Blue LCD Keypad Module
K641+
32-Character Blue LCD Keypad Module
K641R
32-Character Blue LCD Keypad Module with Integrated Card Reader
K641LX
32-Character Blue LCD Keypad with Built-in Transceiver
TM70 Touch
7” Interactive Touchscreen
TM70 Touch
7” Interactive Touchscreen
7-Designer Colours

## Slide 7: Available Motion Detectors Modules
DM50 Dual Element Motion Detector Module
DM60 Quad Element Motion Detector Module
DM70 High-Security Motion Detector Module with Pet Immunity
DG85 Series Outdoor High-Security Digital Motion Detector Module
DG457 Glassbreak BUS Detector
DG467 360° Ceiling Mounted Digital Motion Detector

## Slide 8: Available Zone Expansion Modules
ZX1 1-Zone Expansion Module
ZX4 4-Zone Expansion Module
ZX8 8-Zone Expansion Module
ZX8D Discontinued
ZX16D Discontinued
ZX32D Discontinued

## Slide 9: Available Modules, Special Modules, & Output Expansion Modules
PGM4 4-Output Expansion Module
PRT3 Integration Module
PS25/45 Power Supply Module
HUB2 Hub and Bus Isolator
HUB4D Discontinued
ZC1 Door Contact Module
PMC5 Hand-Held Plug-In Memory Key
307USB Direct Connect Interface
CV4USB RS-485/RS-232 Converter Kit
TEMP07 External Temperature Sensor

## Slide 10: Access Control
EVO systems has a built-in access control Platform With ACM12
R915 Readers
Use your alarm system user database (999 cards)
Manage access to up to 32 doors
1-year holiday schedule
16 access levels
32 (EVO192) User schedules
Simple 4-wire readers and access modules
Log access events
Report Access Events to Monitoring Station [CID]
ACM12

## Slide 11: Access Control
C702
Standard Proximity Card (Clamshell)
C706
ISO Proximity Card
RAC2
2-Way Remote Control with Integrated Access Card
RAC1
Remote Control with Integrated Access Card
C704
Blue Proximity Key Tag
C705
Proximity Key Tags

## Slide 12: Magellan 2-Way Wireless Expansion Module (RTX3)
32 wireless zones per module
RTX3
Up to 999 remote controls with a single module (programmable by the installer and master user)
8 wireless PGMs
Fully supports all Magellan transmitters including 2WPGM and REM2
In-field firmware upgradeable via CV4USB and WinLoad
3 hardwired PGM outputs and 1 optional output

## Slide 13: Wireless Expansion Modules
Remotes
Smoke & Glass Break Detectors
Motion Detectors
Door Contacts
REM3
REM2
REM15
SD360
G550
PMD2P
PMD75
PMD85
DCT10
DCTXP2
DCT2
Wireless PGM
2WPGM

## Slide 14: PCS260/265 GSM/GPRS Communicator Module
Report events to the IPR512 GPRS/IP Monitoring Receiver and/or IPRS-7 GPRS/IP PC Receiver Software
PCS260/265
Report via text message (up to 16 phone numbers)
Control panel communication supervision
End-user can arm or disarm the system by sending a text message (SMS) to the PCS250
Send pre-recorded voice messages to up to 8 telephone numbers to report alarms using the optional VDMP3 Paradox Plug-in Voice Module (GSM mode)
End-user can arm or disarm the system by sending a text message (SMS) to the PCS260/265

## Slide 15: Internet Module (IP150)
Control and monitor your control panel through an IP network (LAN/WAN/Internet)
Send notification of arming/disarming via email
Send notification of system alarms via email
View live status of all zones and partitions via a web browser
Upgrade the firmware of the panel, bus modules or of the IP150 through the Internet
Arm/disarm individual partitions, activate PGMs or I/Os via web browser
Supports static or dynamic IP addresses
Paradox DNS website: www.paradoxmyhome.com
IP150
Multiple Languages supported

## Slide 16: BLUEEYE (for iOS and Android)
Multi-site support: one connection at a time
Arm/disarm system remotely
Control up to 16 PGMs with MG/SP panels and up to 13 with EVO panel (V2.71 and up)
And much, much more!

## Slide 17: Plug-In Voice Dialer (VDMP3)
Dial up to 8 telephone numbers per partition to report events using pre-recorded messages
Arm/disarm the system remotely via telephone
Control PGMs and toggle utility keys remotely via telephone
Voice-guided menus
VDMP3
In-field firmware upgradeable
Connects directly onto the control panel

## Slide 18: Plug-In Voice Dialer (VDMP3)
VDMP3 plugs in directly to the EBUS and SERIAL ports of the EVO panel

## Slide 19: Summary
192-zone system
Up to 999 user codes
8 partitions
Built-in access control (32 doors)
Multibus support
Supports internet module and plug-in voice dialer
Supports wireless expansion
In-field firmware upgradeable
Installer (Babyware) and end-user (NEware) PC software

## Slide 20: Thank You
www.paradox.com